## Slide 1: DRL Induced Glare
An Analytical Study of the Effects
of Peak Luminous Intensity

## Slide 2: NHTSA Proposed Rulemaking August 7, 1998
Federal Motor Vehicle Safety Standard 108:
Lamps, Reflective Devices and Assoc. Equip.
Proposed Rule Change:
Reduction in the maximum permitted
luminous intensity for vehicle daytime
running lights [DRLs]

## Slide 3: Rational for Proposed Rulemaking
400+ complaints re: excessive glare
from U.S. public on file
(N.B. Virtually no complaints in Canada)
“This action is intended to provide the
public with all the conspicuity benefits of
DRL’s while reducing glare”

## Slide 4: U.S. DRL Intensity Specification
Current Maximum: 7000 cd
 compatible with Canadian specification
 compatible with high-beam headlamps
operated at half voltage
 34-inch maximum mounting height
(else 3000 cd – rearview mirror glare)

## Slide 5
Proposed Maximum: 3000 cd (Phase I)
1500 cd (Phase II)
 demonstrated “conspicuity” benefits under
high ambient daytime illumination
(based on “search conspicuity” paradigms)
 minimal discomfort glare
(especially re: rearview mirrors)

## Slide 6: Modeling the Magnitude of Glare Effects
Disability Glare
Adrian & Bhanji (1991) equation
Relative elevation of contrast threshold
Discomfort Glare
deBoer Subjective Rating Scale
Schmidt-Claussen & Bindels (1974) model

## Slide 7: Analytic Conditions
(4) DRL Intensities
1500, 3000, 5000, 7000 cd
(Proposed – Current NHTSA Maximum)
(5) Observation Distances
20, 40, 60, 80, 100 m
(6) Driver Light Adaptation States
1, 50, 100, 500, 1000, 5000
(Dark-to-Brightest Summer Day)

## Slide 8: Driver Luminance Adaptation States
Adaptation Ambient
Time of Day State Illumination
(cd/m2) (lux)
road at night 5 100
twilight / dawn 250 5000
clear winter day 500-1500 10,000-30,000
brilliant summer day 5000 85,000+
Luminance (cd/m2) = illumination (lux) * reflectance / p
assumption: average scene reflectance = 0.15
(asphalt road = 0.10, grass = 0.20)

## Slide 9: Adrian & Bhanji (1991) Disability Glare Model

## Slide 10: Influence of Veiling Luminance (Reduction of Retinal Contrast/Visibility)
Nominal Contrast = Ltarget – Lbackground / Lbackground

## Slide 11: Effects of Glare upon Contrast Sensitivity (Due to Veiling Luminance)
Threshold elevation = Retinal Contrast without Glare
Retinal Contrast with Glare

## Slide 12: 1% Contrast Elevation Factor
Blackwell (1946) showed that small and mid-size objects in the
roadway environment can be detected at a contrast of 1%
across a broad range of photopic luminance levels.
The effect of veiling retinal luminance upon this nominal
detection threshold can be estimated as follows:

## Slide 13: Glare Illumination: Viewing Distance & DRL Intensity

## Slide 14: Disability Glare Drops Rapidly with Increasing Luminance Adaptation
Conclusion:
DRLs can cause some
“disability” at nighttime
but not between
dusk and dawn.
But…What about
“discomfort” glare?

## Slide 15: Discomfort Glare
  deBoer Subjective Rating Scale
  1 Unbearable
  2
  3 Disturbing
  4
  5 Just Acceptable
  6
  7 Satisfactory
  8
  9 Just Noticable

## Slide 16: Schmidt-Claussen & Bindles (1974) Disability Glare Model

## Slide 17: deBoer Discomfort Glare DRL=1500 cd; Changing Adaptation Level
Adaptation Level
Day/Clear Sky
Dusk/Dawn

## Slide 18: deBoer Discomfort Glare DRL=3000 cd; Changing Adaptation Level

## Slide 19: deBoer Discomfort Glare DRL=5000 cd; Changing Adaptation Level

## Slide 20: deBoer Discomfort Glare DRL=7000 cd; Changing Adaptation Level

## Slide 21: Saturn Special Case Alternator Over voltage => 10,000 cd

## Slide 22: DRL Discomfort Borderlines

## Slide 23: European Glare Sensitivity?

## Slide 24: DRL Intensity > 2000 cd Small Gains in Visibility Large Increases in Discomfort